## Slide 1: Project 2 – Cache CS6304 Computer Architecture
Chih-An Chang , William Chang,
  CXC210017, CXC200006
  Department of Computer Science

## Slide 2: Outline
Cache Introduction
Gem5 Setup
CPI Result
Optimize CPI Result
Define Cost Function

## Slide 3
Overview
  What is Cache?
  Why it is important?
Cache Introduction

## Slide 4: What is Cache?
Cache is memory placed in between the processor and main memory.
Cache is responsible for holding copies of main memory data for faster retrieval by the processor.

## Slide 5
Why it so important?
The processor-memory performance gap and results in a computer that can process data much faster than it can retrieve data from memory.
Cache memory stores data for faster access times to help bridge the processor-memory performance gap.

## Slide 6
Overview
  Setup
  Configuration
Gem5
Cache

## Slide 7
Gem5 Setup
1
2
3
4
5
Login to CE6304 linux server
Copy gem5 folder to your local directory
Downloads the Benchmarks
Building Gem5 X86 with Scons
Give permission to run the script
ssh <net-id>@ce6304.utdallas.edu
cp –rf /usr/local/gem5 /home/<netid>/<proj_folder>
git clone https://github.com/timberjack/Project1_SPEC
scons build/X86/gem5.opt –j5
chmod +x ./runGem5.sh

## Slide 8
Cache Configuration
Block size
64 bytes
L2 Cache Category
Unified
CPU Models
TimingSimpleCPU
L1 Cache Category
Separate
Cache levels
2
L1 Instruction Cache Size
128 KB
Unified L2 Cache Size
1 MB
L1 Data Cache Size
128 KB
L1 Instruction Cache Associativity
2-Way
Unified L2 cache
Direct-mapped
L1 Data Cache Associativity
2-Way
Block replacement policy
Least Recent Used (LRU)

## Slide 9
Command Line Parameters
$GEM5_DIR/build/X86/gem5.opt -d ./m5out $GEM5_DIR/configs/example/se.py -c $BENCHMARK -o $ARGUMENT -I 500000000
## CPU types --cpu-type=timing
## Cache Level setting --caches --l2cache
## Setting Cache size --l1d_size=128kB --l1i_size=128kB --l2_size=1MB
## Setting Associativity --l1d_assoc=2 --l1i_assoc=2 --l2_assoc=1
## Setting cache block size --cacheline_size=64

## Slide 10
Overview
429.mcf
401.bzip2
CPI Result

## Slide 11: CPI Calculation
Using “system.cpu.icache.overall_miss_rate::total” × total number of instruction (500,000,000) to get the total miss count is incorrect. We realized that the total number of instructions for D-Cache and L2 Cache can not be 500,000,000.
Find “system.cpu.icache.overall_misses::total” in “stats.txt”
Substitute the parameters into the formula below

## Slide 12
CPI for 429.mcf
L1 miss penalty
6
L2 miss penalty
50
L1 I-cache
Number of miss
676
L1 D-cache
Number of miss
10225985
L2 cache Number of miss
6552122
Total number of Inst
500,000,000
CPI
1.777932132
1

## Slide 13
CPI for 401.bzip2
L1 miss penalty
6
L2 miss penalty
50
L1 I-cache
Number of miss
387
L1 D-cache
Number of miss
4,027,321
L2 cache Number of miss
2,743,240
Total number of Inst
500,000,000
CPI
1.3226633
1

## Slide 14
Overview
How Do We Get Lowest Configuration?
Lowest CPI Configuration
Optimize CPI Result

## Slide 15: How Do We Get Lowest CPI Configuration?
We changed each parameter one at a time, and select the lowest CPI setting
Except for Cacheline size and associativity, the rest of the parameters match the trend that the bigger the size the lower the CPI.
Chart: L1 I-Cache Size
| 2 | 32 | 64 | 128
429.mcf | 1.9859 | 1.778 | 1.7779 | 1.7779
401.bzip2 | 1.3853 | 1.3227 | 1.3227 | 1.3227
Chart: L1 D-Cache Size
| 2 | 32 | 64 | 128
429.mcf | 2.0179 | 1.8456 | 1.8161 | 1.7779
401.bzip2 | 1.389 | 1.3334 | 1.3281 | 1.3227
Chart: L2 Cache Size
| 1 | 2 | 4
429.mcf | 1.7779 | 1.689 | 1.5635
401.bzip2 | 1.3227 | 1.2894 | 1.2656

## Slide 16: How Do We Get Lowest CPI Configuration? – cont.
Chart: Cacheline Size
| 8 | 64 | 128 | 256 | 512
429.mcf | 2.8678 | 1.7779 | 1.5486 | 1.4784 | 1.4869
401.bzip2 | 2.162 | 1.3227 | 1.2023 | 1.1425 | 1.1133
CPI increases while increasing the Cacheline size
Chart: L1 I-Cache Associativity
| 1 | 16 | 32 | 64
429.mcf | 1.7779 | 1.7779 | 1.7779 | 1.7779
401.bzip2 | 1.3227 | 1.3227 | 1.3227 | 1.3227
Chart: L1 D-Cache Associativity
| 1 | 2 | 4 | 8
429.mcf | 1.7953 | 1.7779 | 1.7659 | 1.758
401.bzip2 | 1.3276 | 1.3227 | 1.3214 | 1.3206
Chart: L2 Cache Associativity
| 1 | 1024 | 4096 | 8192 | 16384
429.mcf | 1.7779 | 1.7569 | 1.7569 | 1.757 | 1.7569
401.bzip2 | 1.3227 | 1.3227 | 1.3087 | 1.3087 | 1.3086
CPI increases while increasing the L2 associativity

## Slide 17
Lowest CPI Configuration
 | L1 I-Cache Size | L1 D-Cache Size | L2 Cache | Cacheline Size | L1 I-Cache Associativity | L1 D-Cache Associativity | L2 Cache Associativity | CPI | Cost
401.bzip2 | 128 KB | 128 KB | 4 MB | 512 KB | 16 | 8 | 4096 | 1.07636 | 260.8
429.mcf | 128 KB | 128 KB | 4 MB | 256 KB | 16 | 8 | 4096 | 1.25182 | 260.8

## Slide 18
Overview
Cost Function
  Smallest Cost Configuration
Define Cost Function

## Slide 19
Total Cost
L1-Cache Size (KB)  L1 unit price
L2-Cache Size (MB)  L2 unit price
Total number of associativity  Associativity price
Cost Function
Unit price
Associativity price per way
$0.06
L2 unit price per MB
$0.2
L1 unit price per KB
$0.05

## Slide 20
Smallest Cost Configuration
 | L1 I-Cache Size | L1 D-Cache Size | L2 Cache | Cacheline Size | L1 I-Cache Associativity | L1 D-Cache Associativity | L2 Cache Associativity | CPI | Cost
401.bzip2 | 2 KB | 2 KB | 1 MB | 512 KB | 1 | 1 | 1 | 1.61455 | 0.58
429.mcf | 2 KB | 2 KB | 1 MB | 512 KB | 1 | 1 | 1 | 2.34459 | 0.58

## Slide 21
Overview
  Cost vs. CPI
  Analysis and Conclusion
  Best Cost-Performance Ratio Configuration
Best Cost-Performance Ratio Configuration

## Slide 22: CPI vs. Price
Chart: CPI v.s. Cost
| 1.0763630399999999 | 1.112456656 | 1.113282348 | 1.1192826 | 1.1287382319999999 | 1.1425388320000001 | 1.2023216320000001 | 1.2656309000000001 | 1.2893976 | 1.3086499 | 1.3086644000000001 | 1.3087168 | 1.320601484 | 1.321413232 | 1.3226624 | 1.3226624 | 1.3226624 | 1.3226624 | 1.3226632999999999 | 1.3226632999999999 | 1.3226632999999999 | 1.3226632999999999 | 1.3226632999999999 | 1.322664872 | 1.322666044 | 1.322667544 | 1.327637476 | 1.3280886839999999 | 1.333389744 | 1.3853200800000001 | 1.3889605199999999 | 1.614559552 | 2.1619572959999998
401.bzip2 | 260.8 | 130.64 | 13.3 | 65.52 | 3.7 | 13.3 | 13.3 | 13.9 | 13.5 | 996.28 | 504.76 | 259 | 13.66 | 13.42 | 14.14 | 15.1 | 17.02 | 74.68 | 13.3 | 13.3 | 13.3 | 13.3 | 13.3 | 13.24 | 10.1 | 8.5 | 13.24 | 10.1 | 8.5 | 7 | 7 | 0.58 | 13.3
429.mcf | 260.8 | 4.3 | 130.64 | 65.52 | 13.3 | 13.3 | 13.3 | 13.9 | 13.5 | 74.68 | 259 | 996.28 | 504.76 | 13.66 | 13.42 | 14.14 | 15.1 | 17.02 | 13.3 | 13.3 | 13.3 | 13.3 | 13.3 | 10.1 | 13.24 | 8.5 | 13.24 | 10.1 | 8.5 | 7 | 7 | 0.58 | 13.3
Bad cacheline size config
Bad associativity size config
Based on the plotted chart, we can choose the best cost performance ratio configuration
Best config

## Slide 23: Analysis and Conclusion
      Associativity does not affect much for both benchmarks. In 429.mcf, an extremely high L2 associativity might even increase overall miss count.
      Choosing an appropriate Cacheline Size is important. It can reduce the compulsory misses, but if Cacheline Size is set too big, it starts increasing the overall miss count.
      For both L1 and L2 cache size, the rule is the bigger the better. However, increasing the size of L1 I-Cache is not wise because instruction misses in both benchmarks are low even when the L1 I-Cache size is small, and the cost of L1 cache is high.
      Besides anomalies like extremely high associativity and inappropriate cache line size, investing more cost will give better performance.

## Slide 24
Best Cost-Performance Ratio Configuration
 | L1 I-Cache Size | L1 D-Cache Size | L2 Cache | Cacheline Size | L1 I-Cache Associativity | L1 D-Cache Associativity | L2 Cache Associativity | CPI | Cost
401.bzip2 | 32 KB | 32 KB | 1 MB | 512 KB | 2 | 2 | 1 | 1.12874 | 3.7
429.mcf | 32 KB | 32 KB | 4 MB | 256 KB | 2 | 2 | 1 | 1.26722 | 4.3

## Slide 25: Thank you